## Slide 1: 介面電路_七段顯示器
2024/10/14

## Slide 2: 例一 七段+門閂
https://falstad.com/circuit/circuitjs.html?ctz=CQAgjCAMB0l5AWAnC1b0DZwwExxwOwEDMkAHDhigSAKyR10O0CmAtGGAFAJhkgI4IDmBwhitMSLEMIgxg0XRaIAA4BLAHYAdAM7de-QQzZkGEqWajgBza0pUadunDz62TCfheFfrcu0UoZTUtPWI3IyEOLB8Y-1sFexCnPQRIj3BYySyE+RUgmEcw3VoMsCQxHBwEcARa6trZRILk4udRcsrwbrB6npkbfPtg9r1OLrEwDFl+6aCApIdQjsgM4xArHytm4cKUkoJ1oT8fP13AtpW9DEmQHFosPobHvMvl1P0IsFoaZCxpHQcPxAQwaIouNMoiYwAQsLwAbCsHhaLV+IURq01gB3ARIJ5YR6yLA4vHw-i0brnLi4-6bBgYGr0qA0uhUim9EmsxlohlM6YsgAymQ4cPuBCkSJGADMAIYAG10LAUXCAA
https://tinyurl.com/25bhfxv5

## Slide 3: 程式碼
int i;
void setup() {
Serial.begin(115200);
// add external voltage (Javascript) with name "pin n" to access output pins
for (i=1;i<8;i++) {
pinMode(i,OUTPUT);
}
}
void loop() {
Serial.println("looping");
for (i = 1; i != 8; i++) {
digitalWrite(i, HIGH);
delay(50);
digitalWrite(i, LOW);
}
}

## Slide 4: 例二 並聯顯示
https://falstad.com/circuit/circuitjs.html?ctz=CQAgDOB0YzCsIBsBOSBmALBgjGu2wNNtEE4IyKBTAWm2wCgcAOEAJgwhrUVe2TYhuvcCGwhOIBBBmQEABwCWAOwA6AZ0Yt2k7jzEChafRHGTposHJBK16tk2ysOXNIQODu70xIqWoCioaaI7OumwA7IL8npGCPub+VoF2GKE6XC4eQlkJfjIBNkHqcOlZdBGI2RVVeVJJ1rYaEWXhYHyGNGztomb5lo3FiAzYcBFSiK4icJ08rBDjMiMiGIgYQkSCGMxcm+xgcOvzSfUFYAwA7hOZkogcOZLnV3CTOT2kVV09T9dC2JVIZisGrgS5IF5vVgfB5LK68YH-KrwmGggAyGQ2aGi2E8ex8ADMAIYAG3UVFOYORiMBfBxoLhEOwWHBVXo8TBL1MAKpAJ+nLEzOhTPWfNebKQ93F5xIrFW6xoOwkioVEG6hxAxzOp0sIzGvzoVRmnhIokW9IkayEir2KvNNutWMx7KucqdEkdNDxYJte3KXpdloNvi4Jp+nBDVXDRhEPzQzHlxiqcfWoe9lpNybEtTT622IDmSvNBbzBa8IrBeEEisrOSidst1bgVdhFpTdMTYjpsf04o7XUeFe6AvWWMy3xzw-zQ+F9ZTALcc+zVwXYnn7hBYZg0bCU3mFfjRn05Q7sZEZYx59jTdrgnKcSL+n7qvCA+XQ6+O8hRfX1PK1LDgbUiuG4Th+U5jnuAbylkfa5KB941l0dYAQm7iliuKGHkmB56EurbbsGBHnEAA
https://tinyurl.com/2dl3tbkj

## Slide 5: 程式碼
同前

## Slide 6: 同時顯示1、2(不控制門閂LD)
電路圖同上
程式碼：
int i;
void setup() {
Serial.begin(115200);
// add external voltage (Javascript) with name "pin n" to access output pins
for (i=1;i<8;i++) {
pinMode(i,OUTPUT);
}
}
void loop() {
Serial.println("looping");
//1
digitalWrite(2, HIGH);
digitalWrite(3, HIGH);
delay(50);
digitalWrite(2, LOW);
digitalWrite(3, LOW);
//2
digitalWrite(1, HIGH);
digitalWrite(2, HIGH);
digitalWrite(4, HIGH);
digitalWrite(5, HIGH);
digitalWrite(7, HIGH);
delay(50);
digitalWrite(1, LOW);
digitalWrite(2, LOW);
digitalWrite(4, LOW);
digitalWrite(5, LOW);
digitalWrite(7, LOW);
}

## Slide 7: 閃爍顯示1、2(控制門閂)
https://falstad.com/circuit/circuitjs.html?ctz=CQAgDOB0YzCsIBsBOSBmALBgjGu2wNNtEE4IyKBTAWm2wCgcAOEAJgwhrUVe2TYhuvcCGwhOIBBBmQEABwCWAOwA6AZ0Yt2k7jzEChafRHGTposHJBK16tk2ysOXNIQODu70xIqWoCioaaI7OumwA7IL8npGCPub+VoF2GKE6XC4eQlkJfjIBNkHqcOlZdBGI2RVVeVJJ1rYaEWXhYHyGNGztomb5lo3FiAzYcBFSiK4icJ08rBDjMiMiGIgYQkSCGMxcm+xgcOvzomRJ4AwA7hOZkogcOZJgl9c5PaRVXT1PV3CTQtiVJDMVg1c5Xd6vVgQrqPZ68EEAqrwh5LcHAsSA5H0eJw35iLBIPHYsEvRFAviA76kgkQ7AEqm-UzYQR3dbEp4kVirdY0HYSPm8iDdQ4gY6nPwWUqjcaM-5VGaeEiiRYk7lCPl7QWqtYbNBbPW6nFXTV7cp7KlquhVThcJUWmBy3xTebPNDMHnGKputm1Z5qpXesS+4067YgOb8kkRsMRrzrKl4QR8xM5KLao4QFN8i064mesTMqP6PP6GGo8PdfHrPWZL5+3MEmtV9MYr3uMkJ9uAtw8jt+h3CMLOqPuoz6cr5hMiOMZIzeV1wWJp8pxIsfLIr2FXJufIeQqPuUHlPsh3vdw8niQ63cV2su08o8Ol3L1nmrlNdNM5j3uWM9lt6F6o6AQB0YDhGTzaGaBoxIavS+PUBTJEUdj0K0XB8rBWp1BYsgpBozJ+gaWrlNmDBAA
https://tinyurl.com/26gsaaew

## Slide 8: 程式碼
int i;
void setup() {
Serial.begin(115200);
// add external voltage (Javascript) with name "pin n" to access output pins
for (i=1;i<8;i++) {
pinMode(i,OUTPUT);
}
pinMode(11,OUTPUT);
pinMode(12,OUTPUT);
}
void loop() {
Serial.println("looping");
//1
digitalWrite11,HIGH);
digitalWrite(2, HIGH);
digitalWrite(3, HIGH);
delay(50);
digitalWrite(2, LOW);
digitalWrite(3, LOW);
digitalWrite(11,LOW);
//2
digitalWrite(12,HIGH);
digitalWrite(1, HIGH);
digitalWrite(2, HIGH);
digitalWrite(4, HIGH);
digitalWrite(5, HIGH);
digitalWrite(7, HIGH);
delay(50);
digitalWrite(1, LOW);
digitalWrite(2, LOW);
digitalWrite(4, LOW);
digitalWrite(5, LOW);
digitalWrite(7, LOW);
digitalWrite(12,LOW);
}

## Slide 9: 穩定顯示1、2(控制門閂)
https://falstad.com/circuit/circuitjs.html?ctz=CQAgDOB0YzCsIBsBOSBmALBgjGu2wNNtEE4IyKBTAWm2wCgcAOEAJgwhrUVe2TYhuvcCGwhOIBBBmQEABwCWAOwA6AZ0Yt2k7jzEChafRHGTposHJBK16tk2ysOXNIQODu70xIqWoCioaaI7OumwA7IL8npGCPub+VoF2GKE6XC4eQlkJfjIBNkHqcOlZdBGI2RVVeVJJ1rYaEWXhYHyGNGztomb5lo3FiAzYcBFSiK4icJ08rBDjMiMiGIgYQkSCGMxcm+xgcOvzomRJ4AwA7hOZkogcOZJgl9c5PaRVXT1PV3CTQtiVJDMVg1c5Xd6vVgQrqPZ68EEAqrwh5LcHAsSA5H0eJw35iLBIPHYsEvRFAviA76kgkQ7AEqm-UzYQR3dbEp4kVirdY0HYSPm8iDdQ4gY6nPwWUqjcaM-5VGaeEiiRYk7lCPl7QWqtYbNBbPW6nFXTV7cp7KlquhVThcJUWmBy3xTebPNDMHnGKputm1Z5qpXesS+4067YgOb8kkRsMRrzrKl4QR8xM5KLao4QFN8i064mesTMqP6PP6GGo8PdfHrPWZL5+3MEmtV9MYr3uMkJ9uAtw8jt+h3CMLOqPuoz6cr5hMiOMZIzeV1wWJp8pxIsfLIr2FXJufIeQqPuUHlPsh3vdw8niQ63cV2su08o8Ol3L1nmrlNdNM5j3uWM9lt6F6o6AQB0YDhGTzaGaBoxIavS+PUBTJEUdj0K0XB8rBWp1BYsgpBozJ+gaWrlNmDBAA
https://tinyurl.com/26gsaaew

## Slide 10: 程式碼
int i;
void setup() {
Serial.begin(115200);
// add external voltage (Javascript) with name "pin n" to access output pins
for (i=1;i<8;i++) {
pinMode(i,OUTPUT);
}
pinMode(11,OUTPUT);
pinMode(12,OUTPUT);
}
void loop() {
Serial.println("looping");
//1
digitalWrite(11,HIGH);
digitalWrite(2, HIGH);
digitalWrite(3, HIGH);
delay(50);
digitalWrite(11,LOW);
digitalWrite(2, LOW);
digitalWrite(3, LOW);
//2
digitalWrite(12,HIGH);
digitalWrite(1, HIGH);
digitalWrite(2, HIGH);
digitalWrite(4, HIGH);
digitalWrite(5, HIGH);
digitalWrite(7, HIGH);
delay(50);
digitalWrite(12,LOW);
digitalWrite(1, LOW);
digitalWrite(2, LOW);
digitalWrite(4, LOW);
digitalWrite(5, LOW);
digitalWrite(7, LOW);
}